#include <LiquidCrystal.h>
/*
* Display5vOrless sketch
* prints the voltage on analog pin to the serial port
* Warning - do not connect more than 5 volts directly to an Arduino pin.
*/
LiquidCrystal lcd(12, 11, 5, 4, 3, 2);
const float referenceVolts = 5.0; // the default reference on a 5-volt board
const int batteryPin = 0; // battery is connected to analog pin 0

void setup()
{
Serial.begin(9600);
lcd.begin(16,2);
}

void loop()
{
int val = analogRead(batteryPin); // read the value from the sensor
float volts = (val / 1023.0) * referenceVolts; // calculate the ratio
lcd.setCursor(0,0);
lcd.print("volts");!
Serial.println(volts); // print the value in volts
delay(1000);
}